## Slide 1
Team Name : Logic Builders
BRILLIANCE@SCALE
Team Members Names | Engineering Specialisation | Graduating Year | College Names
Meghma Das | Information Technology | 2027 | MCKV Institute of Engineering
Argha Pal | Information Technology | 2027 | MCKV Institute of Engineering

## Slide 2
Tell Us a Bit About Yourself
BRILLIANCE@SCALE
 | Meghma Das | Argha Pal
Any projects you've worked on | Movie Recommendation System, AI tutoring system for rural India, Meeting Schedular Agent | Movie Recommendation System, AI tutoring system for rural India, Health Coach Agent
Past Hackathon experiences | Smart India Hackathon 2024, Smart India Hackathon 2025, Infosys Global Hackathon 2025, Brain Dead 2k26 | Smart India Hackathon 2024, Smart India Hackathon 2025, Brain Dead 2k26
Accolades or awards received | NA | NA
Other details (If any) | NA | NA

## Slide 3
Problem Statement 3: Driving Behavior Score
BRILLIANCE@SCALE
Solution Overview
RideIQ is a real-time two-wheeler driving behavior scoring system using low-cost sensor fusion (IMU + GPS) and a jerk-based scoring algorithm.
Sensors:
MPU-6050 IMU + NEO-6M GPS + Barometer on ESP32
Algorithm:
Weighted jerk-based scoring across 5 parameters
Real-time:
Score updated every 5 seconds via BLE/Wi-Fi
Cost:
Total Bill Of Material under ₹1,000 per unit
Output:
Dashboard, cloud log, insurance & fleet integration
Key Differentiators
Context-aware scoring
(speed zone + road type)
Kalman filter IMU+GPS
fusion for lean angle
Jerk-based thresholds
(mathematically grounded)
Adaptive baseline learns
rider over first 5 trips
No internet required
(edge inference on ESP32)

## Slide 4
BRILLIANCE@SCALE
Sensors Details
A single chip combines three-axis accelerometer with three-axis gyroscope (6-axis) sensor. It uses I2C for communication via the address 0x68 (or 0x69 if the AD0 pin is set to true). It features an integrated Digital Motion Processor (DMP) that performs sensor fusion calculations to take the load off of the ESP32 and can provide quaternions directly as output. The IC runs on 3.3V to 5V power supply and can be connected to any of the 3.3V headers on the ESP32.
When looking for a barometric altitude sensor, the BMP280 and MS5611 are two of the most common options. The BMP280 has a pressure sensing range between 300 and 1100 hPa and an altimetry resolution of approximately giving it a great general use sensor. The MS5611 has a wider range of pressure measurements and its altimetry resolution is significantly better than the BMP280 making it the preferable option for drones and higher precision applications. Both sensors can be connected to an MPU-6050 using I2C or SPI comms and also have a built-in temperature sensor in addition to measuring altitude through the use of the barometric formula. Because both sensors use unique I2C addresses, they can share I2C SDA and SCL lines with an MPU-6050 while all three sensors communicate on the same I2C network.
A u-blox GNSS receiver that provides output via NMEA 0183 sentences through the UART serial port with a default baud rate of 9600. It will provide approximately 2.5 m circular error probable (CEP) accuracy when there is an unobstructed view of the sky above. It requires a supply voltage of 3.3 V and a ceramic patch antenna (the antenna is typically soldered to it) oriented in a vertical position to receive signals from satellites to establish a position fix. Cold-start position fixes can take 30 to 60 seconds to establish.

## Slide 5
Design Details
BRILLIANCE@SCALE
Market Research & Literature Survey
• India has 300M+ registered two-wheelers; two-wheelers account for ~35% of all road fatalities (MoRTH 2023)
• Existing OBD-based systems (Mfine, Acko, Bajaj Allianz) work only for 4-wheelers; no affordable two-wheeler solution exists
• UBI (Usage-Based Insurance) market projected to reach $28B globally by 2027 — two-wheelers are an untapped segment
Working Principle & Scoring Formula
Score = 100 − Σ (penaltyᵢ × weightᵢ) where jerk J = dA/dt (m/s³) | lean angle θ = ∫ gyro_z dt − GPS_heading_correction
Parameter | Trigger Threshold | Weight | Score Penalty
Harsh braking | J < −15 m/s³ | 25% | −10 per event
Hard acceleration | J > +12 m/s³ | 20% | −8 per event
Sharp cornering | θ > 35° | 25% | −10 per event
Speed limit violation | >120% of limit | 20% | −5 per km
Lane stability | Lateral jerk > 8 | 10% | −3 per event

## Slide 6
Design Details — Algorithm Logic Flow Diagram
BRILLIANCE@SCALE
End-to-end data flow: from raw sensor input to final driving behavior score
IMU
MPU-6050
Accel + Gyro
100 Hz
GPS
NEO-6M
Speed + Heading
10 Hz
Baro
BMP280
Altitude + Incline
25 Hz
Kalman Filter — Sensor Fusion
Merges IMU + GPS to estimate: velocity, lean angle θ, jerk J = dA/dt | removes noise & GPS lag
Brake detect
J < −15 m/s³
→ HarshBrake event
Corner detect
θ > 35°
→ SharpCorner event
Accel detect
J > +12 m/s³
→ HardAccel event
Context Engine
OSM road class
Speed zone tag
Time of day
Weighted Scoring Engine
Score = 100 − Σ(penaltyᵢ × weightᵢ)
Brake 25% · Accel 20% · Corner 25% · Speed 20% · Stability 10% → Score 0–100 (updated every 5 s)

## Slide 7
Design Details — System Architecture & Benchmarking
BRILLIANCE@SCALE
Hardware block diagram
ESP32
MCU
MPU-6050
IMU
NEO-6M
GPS
BMP280
Baro
LED
Alert
BLE
App
Wi-Fi
Cloud
I²C / SPI
UART
BLE/WiFi
Benchmarking vs existing solutions
Feature | RideIQ | Others
2-wheeler specific | ✓ | ✗
Works offline | ✓ | ✗
Lean angle tracking | ✓ | ✗
Cost < ₹1,000 | ✓ | ✗
Real-time alert | ✓ | Partial
Context-aware scoring | ✓ | ✗
Jerk-based (not G-force) | ✓ | ✗

## Slide 8
Logic Flow Diagram — Real-Time Scoring Pipeline
BRILLIANCE@SCALE
Data acquisition
Processing
Scoring engine
Output
IMU — MPU-6050
Ax, Ay, Az @ 100Hz · Gx, Gy, Gz
GPS — NEO-6M
Lat/Lon, Speed, Heading @ 10Hz
Barometer — BMP280
Altitude Δ → road incline %
Context DB (OSM)
Road class · Speed limit zone
Kalman Filter
Fuse IMU + GPS, reduce noise/drift
Jerk Computation
J = ΔA/Δt (m/s³) per axis
Lean Angle Est.
θ = ∫Gz dt − GPS heading corr.
Event Detector
Threshold crossing → event flag
Context Tagger
Speed zone + road class lookup
Braking Score
Penalty = f(|J|, freq) wt=25%
Acceleration Score
Penalty = f(|J|, freq) wt=20%
Cornering Score
Penalty = f(θ, G-force) wt=25%
Speed Score
Penalty = f(v/limit) wt=20%
Stability Score
Penalty = f(lateral J) wt=10%
Weighted Sum
S = 100 − Σ(pᵢ×wᵢ)
Adaptive Baseline
Calibrate to rider over 5 trips
Score = 0–100
Updated every 5 seconds
BLE → Rider App
Live score + trip summary
MQTT → Cloud
Log, insurance, fleet dash
Score < 40 → Buzzer Alert

## Slide 9
Major Risks & Mitigation
BRILLIANCE@SCALE
RISK:
IMU drift over long rides
High
✓ Kalman filter with periodic GPS re-calibration every 60s
RISK:
False positives on speed bumps / potholes
Medium
✓ Barometer + accelerometer Z-axis filter distinguishes road anomalies from braking
RISK:
GPS signal loss in urban canyons
Medium
✓ Dead reckoning using IMU integration maintains scoring continuity for up to 30s
RISK:
Battery drain on ESP32
Low
✓ Deep sleep mode between events; duty cycle reduces power to <80mA average
RISK:
Rider behavior varies by region/road type
High
✓ Adaptive baseline + OSM-based road context engine normalizes scoring per road class

## Slide 10
Business Potential
BRILLIANCE@SCALE
₹4,200 Cr+
India UBI market
(2026E)
300M+
Registered 2-wheelers
in India
35%
Road fatalities
from 2-wheelers
₹1,000
Hardware Bill Of Material
per unit
Revenue Model & Market Segments
B2B — Insurance Companies
UBI premium discounts drive rider adoption; insurers pay ₹50–100/month per device subscription
B2B — Fleet Operators (Zomato, Swiggy, Dunzo)
Reduce accident liability; driver score used for bonuses & training
B2C — Rider Safety App
Freemium app; premium tier at ₹99/month unlocks detailed trip analysis
B2G — Smart City / Traffic Dept
Aggregate anonymized data for hotspot analysis and road safety policy

## Slide 11
Plan & Budget Needed
BRILLIANCE@SCALE
Prototype Development Milestones
Month 1
Hardware Setup
ESP32 + IMU + GPS assembly; basic data logging
Month 2
Algorithm Dev
Kalman filter + jerk detection; MATLAB simulation
Month 3
Field Testing
Real-ride data collection; threshold calibration
Month 4
App & Cloud
BLE app; MQTT cloud dashboard; UX testing
Month 5
Validation
Benchmarking vs existing; accuracy report
Budget Required for Prototype
Item | Estimated Cost
Hardware (ESP32, IMU, GPS, barometer ×3 units) | ₹3,500
PCB fabrication & enclosure (weatherproof) | ₹4,000
Cloud hosting (AWS IoT / Firebase — 6 months) | ₹2,500
App development (React Native) | ₹0 (in-house)
Testing & field data collection | ₹2,000
Contingency (10%) | ₹1,200
TOTAL | ₹13,200

## Slide 12
VARROC eureka CHALLENGE
Thank You
Team Logic Builders | Problem Statement 3: Two-Wheeler Driving Behavior Score
BRILLIANCE@SCALE